## Slide 1
Polar Codes:
A New Way Of Achieving Shannon Capacity
Prepared by Lab Group 6 - Group 1

## Slide 2
Honor Code
We declare that
→ The work that we are presenting is our own work.
→ We have not copied the work (the code, the results, etc.) that someone else has done.
→ Concepts, understanding and insights we will be describing are our own.
→ We make this pledge truthfully. We know that violation of this solemn pledge can carry grave consequences.

## Slide 3
Attested by:

## Slide 4
Group Members
Aditya Desai (202201451)
Dev Vyas (202201453)
Srushti Makwana (202201458)
Harsh Popatiya (202201463)
Hardi Naik (202201477)
Anuj Valambhiya (202201481)
Nandini Mandaviya (202201487)
Hitanshu Variya (202201510)
Jainam Patel (202201514)
Heer Shah (202201525)
Dhruvin Chaudhary (202101239)

## Slide 5
An analogy to understand Polar Codes
Why Polar Codes?
II
III
IV
7
8
Page
Table of
Contents
Introduction
I
6
Polar Transformation
9
Encoding Algorithm
Decoding Algorithm
How Polar Codes work?
VII
VI
27
35
13
IX
AWGN and BPSK
VIII
33
Decoder Comparison Output
X
65
Appendix
XI
75
References
XII
84
Theory of Polarization
12
V

## Slide 6
Polar Codes were discovered by Erdal Arikan in 2008. They have become the most favourable codes for Forward Error Correction since then. They are notable for being first in their types with provable capacity-achieving property. Polar codes have especially found their application in the 5G wireless communication.
6
Introduction
“Polar Codes were not invented, they were discovered.”
~Erdal Arikan

## Slide 7
An Analogy to
Understand Polar Codes

## Slide 8
8
Polar codes propose a new approach to achieve the Shannon capacity. Instead of encoding data bits like traditional methods, polar codes polarize the channel into two extreme channels: highly reliable and less reliable. They then utilize the highly reliable channels to transfer the data bits, unlike different pre-existing coding techniques that focus on encoding the data bits. Thus, Polar Codes provide ease by working directly over channels rather than the data bits.
Why Polar Codes?

## Slide 9
Polar
Transformation

## Slide 10
10

## Slide 11
11

## Slide 12
Theorem of Polarization

## Slide 13
How Polar Codes work?

## Slide 14
Erikan’s
14

## Slide 15
15
(Using the chain rule)
Notes: U1 and U2 are IIDs

## Slide 16
16

## Slide 17
17

## Slide 18
18

## Slide 20
20
Polarization Martingale

## Slide 21
21
Methodology
Polarization of BEC(1/2) for N=16

## Slide 22
Polarization of BEC Rate (1/2) N=64
22

## Slide 23
Bar Chart
23
Research Results
Polarization of BEC Rate (1/2) N=256

## Slide 24
24
Polarization of BEC(1/2) for N=1024

## Slide 25
25

## Slide 26
Observations :
  In polar codes, as the value of N (representing the number of channels) increases, the number of channels approaching capacity extremes (0 or 1) also increases.
  We observe a greater quantity of extreme channels compared to mediocre ones.
  Polar codes strategically allocate frozen bits to channels with poor performance (the "worst" channels) and reserve efficient channels for transmitting message bits.
  This allocation minimizes error probability by leveraging channel characteristics.
  As N tends towards infinity, the error probability diminishes significantly, converging towards Shannon capacity.
  This demonstrates the remarkable efficiency and effectiveness of polar codes in maximizing transmission reliability.
26

## Slide 27
Encoding Algorithm

## Slide 28
  It is a sequence which gives a sorted order of channels starting from worst channels to the best channels according to the efficiency of the output.
  For N=16 the reliability sequence is:
1 2 3 5 9 4 6 10 7 11 13 8 12 14 15 16
  The reliability sequence is derived using the Bhattacharya Parameter, which is defined as below:
Reliability Sequence:
28

## Slide 29
Hypothesis 3
29
Suppose we have a message m having K bits. We need to generate a codeword C having N (N=2 )bits.
Algorithm:
  Find first N-K worst channels for N based on the reliability sequence.
  For all the N-K positioned indexes in the vector u we set the bits to zero. These positions are also known as Frozen Positions.
  Set the remaining K bits of vector u as the message bits.
  Now, to generate the final codeword or the encoded message we need to multiply vector u with the Generator Matrix G based on the polar transform defined earlier.
n
n
Example:
  Message m: 4 Bits (K=4)
  Codeword C: 8 Bits (N=2 )
  Reliability Sequence: 1 2 3 5 4 6 7 8
3
n
Codeword C = u.G

## Slide 30
2
4
5
3
6
7
1
2
3
0
0
1
0
1
0
m1
m3
m2
0
0
0
0
m4
[0 0]
[m2 m2]
[m3+m4 m4]
[m1 m1]

## Slide 31
[m2+m3+m4 m2+m4 m3+m4 m4]
2
4
5
3
6
7
1
2
3
0
0
1
0
1
0
m1
m3
m2
0
0
0
0
m4
[0 0]
[m2 m2]
[m3+m4 m4]
[m1 m1]
[m1 m1 m1 m1]

## Slide 32
2
4
5
3
6
7
1
2
3
0
0
1
0
1
0
m1
m3
m2
0
0
0
0
m4
[0 0]
[m2 m2]
[m3+m4 m4]
[m1 m1]
[m2+m3+m4 m2+m4 m3+m4 m4]
[m1 m1 m1 m1]
C=[m1+m2+m3+m4 m1+m2+m4 m1+m3+m4 m1+m4 m2+m3+m4 m2+m4 m3+m4 m4]

## Slide 33
AWGN and BPSK

## Slide 34
34
For a BPSK Channel the bit conversion scheme is
1 is converted to -1
0 is converted to 1
G4
BPSK
+
AWGN
u1
u3
u4
u2
x1
x2
x3
x4
r3
r2
r1
r4
AWGN is added during transmission

## Slide 35
Decoding Algorithm

## Slide 36
Successive Cancellation Decoding
36
Basic Building Block N=2 SC Decoder
Proof of SISO SPC decoder and SISO Repetition decoder in Appendix
There are two main functions we require for Successive Cancelation Decoder. They can also be described as two types of SISO decoders used in different parts of the SC decoding algorithm. They are as described below:

## Slide 37
37
u1
u2
r = [r1 r2] x=[x1 x2]
f(r1,r2)
u1
u2
r = [r1 r2]
u1
u2
x̂=[û1+û2 û2]
Step 1
Step 2
Step 3
û1
g(r1,r2,û1)
û1
û2
We repeat the above three steps till we traverse the whole tree (For N>2)
Successive Cancellation Decoding(N=2)

## Slide 38
38
L = [L1 L2 ..... LM]
f(L(1:M/2),
L(1+M/2:M))
Step L
Step R
Step U
û1
g(L(1:M/2),
L(1+M/2:M),
û1)
û1
û2
We repeat the above three steps till we traverse the whole tree (For N>2)
M = 2
m
f(a(1:p),b(1:p))=[f(a1,b1)f(a2,b2) ...f(ap,bp)]
[û1+û2 û2]
M/2 values
M/2 values
M/2 bits
M/2 bits each
M bits
g(a(1:p),b(1:p),c)=[g(a1,b1,c1)g(a2,b2,c2) ...g(ap,bp,cp)]
Here f and g functions are the same as defined earlier
Successive Cancellation Decoding(for any N)

## Slide 39
39
We repeat the above step for all the leaf nodes till we traverse the whole tree (For N>2)
If ‘i’ is a Frozen Position: ûi=0
L(ui)
ûi
ui
If ‘i’ is a message Position:
ûi=0, if L(ui) ≥ 0
ûi=1, if L(ui) < 0
Successive Cancellation Decoding(for any N)

## Slide 40
40
Start at the root.
  Do step L and go to the left child.
2. Once the decision (û1) is recieved from the left child, do step R and go to the right child
3. When decision is received from the right child (û2), do step U and go to the parent.
Algorithm:
For intermediate nodes
For Leaf nodes
Leaf must make a decision and send it to the parent
Successive Cancellation Decoding

## Slide 41
Simulating Outputs

## Slide 42
42

## Slide 43
43

## Slide 44
44

## Slide 45
Functionality Test

## Slide 46
46

## Slide 47
47

## Slide 48
Block_Error_Rate
48

## Slide 49
49
Successive Cancellation Decoding : `Disadvantages
  SC requires the decoding process to advance bit by bit. This results in high latency and low throughput when implemented in hardware [cite].
  Polar codes decoded with SC only achieve the channel capacity when the code length tends toward infinity. For practical polar codes of moderate length, SC decoding cannot provide a reasonable error-correction performance.
  SCL Decoder is about 1dB better than SC decoder.

## Slide 50
Successive Cancellation List : Decoding Block Diagram
(N,K) code
CHECK CRC
Add CRC
BPSK
+
AWGN
LIST DECODER
EncodeR
msg
A
bits
K bits
N bits
M : list size
M codeword
Estimated Message
50

## Slide 51
Cyclic Redundancy Check (CRC)
  CRC is a method to detect error in digital networks. It is used to change accidental changes in data.
  In this method, we divide the message by a selected polynomial to get a remainder polynomial which we then append it to the end of message to form our new codeword which we then transmit.
  On the receiver side, after decoding, we divide decoded codeword by the selected CRC polynomial.
  If the remainder on division comes out to be zero then it is a valid codeword.
51

## Slide 52
Path metric:
Sum of decision metrics for every path is called Path metric.
52

## Slide 53
53
Algorithm:
  Here we use as many SC decoders as our list size (L) and run them together.
  We follow the same procedure as SC decoder for all the concurrent decoders except at the leaf.
  At the leaf we do following extra procedures as follows:
  We consider all possible estimated bits for a given belief
  We keep track of path metric in which we assign a penalty (absolute value of belief) for taking an opposite decision for a given belief.
  Then we sort and take the first L decoders having minimal path metrics.
  After we receive the L decoded codewords we perform a CRC check.

## Slide 54
Possible scenarios during CRC check on L decoded codewords
54
When none of the codewords yield zero remainder
When only 1 of the codeword yield zero remainder
When more than 1 codewords yield zero remainder
Choose codeword with minimum path metric
Select that codeword
Choose codeword with minimum path metric

## Slide 55
SC decoder 1
PM = 0
u1
SC decoder 2
DM (1)
SC decoder 1
DM (0)
u2
u2
0
1
0
1
1
0
1
1
SC decoder 4
DM (1) + DM (1)
1
22
SC decoder 3
DM (1) + DM (0)
1
22
SC decoder 2
DM (0) + DM (1)
1
12
SC decoder 1
DM (0) + DM (0)
1
12

## Slide 56
SC decoder 1
PM 1
SC decoder 2
PM 2
SC decoder 3
PM 3
SC decoder 4
PM 4
ui
ui
ui
ui
1a : PM1 + DM1i(0)
2b : PM2 + DM2i(1)
3a : PM3 + DM3i(0)
3b : PM3 + DM3i(1)
4a : PM4 + DM4i(0)
4b : PM4 + DM4i(1)
1b : PM1 + DM1i(1)
2a : PM2 + DM2i(0)
ui+1
ui+1
ui+1
ui+1
X
X
X
X
1
0
1
0
1
0
1
0

## Slide 57
Simulating Outputs

## Slide 58
58

## Slide 59
59

## Slide 60
60

## Slide 61
Simulating for different (N,K)’s

## Slide 62
62

## Slide 63
63

## Slide 64
Block_Error_Rate
64

## Slide 65
Decoder Comparison Outputs

## Slide 66
65

## Slide 67
67

## Slide 68
68

## Slide 69
Comparing
Functionality Test

## Slide 70
70

## Slide 71
71

## Slide 72
72

## Slide 73
Analyzing the Differences Between
Polar Codes and LDPC Codes

## Slide 74
1. Shannon capacity:
  LDPC: Operates near the Shannon limit for high reliability.
  Polar: Can match Shannon capacity in ideal scenarios.
2. BER:
  Polar: Low BER for short messages.
  LDPC: Superior BER for long messages.
3. Throughput:
  LDPC: High throughput, ideal for large data volumes.
  Polar: Potential throughput limitations for extensive data streams.
4. Latency:
  Polar: Lower latency, suitable for real-time applications.
  LDPC: Slightly higher latency, especially for time-sensitive tasks.
Factors:
74

## Slide 75
Appendix

## Slide 76
SISO Decoder for SPC
76

## Slide 77
77

## Slide 78
78

## Slide 79
79

## Slide 80
80

## Slide 81
SISO Decoder for Repetition Code
81

## Slide 82
82

## Slide 83
83

## Slide 84
References
  Polar Codes in 5G Standard by Prof. Andrew Thangaraj
  Essence of Polar Codes by Dr. Erdal Arikan
  Flesh of Polar Codes by Dr. Emre Telatar
  Summary on Polar codes by Prof. Tufail Ahmad
  Slides by Dr. Erdal Arikan
  Channel Polarization: A Method for Constructing Capacity-Achieving Codes for Symmetric Binary-Input Memoryless Channels
  On the rate of Channel Polarisation
  Source Polarisation by Dr. Erdal Arikan
  A Brief Introduction to Polar Codes by Dr. Henry Pfister
  Simplified Calculation of Bhattacharyya Parameters in Polar Codes
  Polar codes: Primary concepts and practical decoding algorithms
84

## Slide 85
Thank You!